Experiment: Speed of Muons (PART 1)

- Aim of the experiment:

The aim of the experiment is an investigation of the probability of two coincidental hits in a given time for two parallel plates, setup one above the other.

- Equipment and setup:

We used

  - two plates, each including a scintillator and a photomultipliertube (PMT)

  - Data Acquisition Card (DAC) developed by Quarknet

  - GPS receiver

  - pc

DAC

- Procedure

We placed the plates one above the other.

During a time of a few hours, we measured the number of hits on each plate.

Beside that, when a plate was hit, a time-window of 192 ns ( = 8 x 24 ns) was opened. If a second hit was registered in this time (on the other plate), a `coincidence`-event was noted.

So, the time of the experiment, also the number of coincidence was measured.

Finally, we got 3 series of data:

1: number of hits on CH1 (per minut)

2: number of hits on CH2 (per minut)

3: number of coincidences (per minut)

- Results

| CH1: 1150 | hits / min | (average) |
| --- | --- | --- |

| CH2: 4074 | hits / min | (average) |
| --- | --- | --- |

| Number of coincidences: 90 | / min | (average) |
| --- | --- | --- |

The big difference between the average number of hits on CH1 and CH2 has to do with the adjustement and the sensibility of the two plates and the PMT.

- Analyze

| CH1: 1150 | hits / min |  |  |
| --- | --- | --- | --- |

The average number of hits in 192 ns is 0.00000368.

The numbers we count are supposed to be Poisson-distributed:

P (k, λ) =

k = number

λ = average

So we can calculate the probability of getting 0, 1, 2 …. hits in  Δt = 192 ns.

| k | Probability | Prob (%) |
| --- | --- | --- |
| 0 | 0.999996 | 99.9996 |
| 1 | 3.68E-06 | 0.000368 |
| 2 | 6.77E-12 | 6.77E-10 |
| 3 | 8.31E-18 | 8.31E-16 |
| 4 | 7.64E-24 | 7.64E-22 |
| 5 | 5.62E-30 | 5.62E-28 |
| 6 | 3.45E-36 | 3.45E-34 |
| 7 | 1.81E-42 | 1.81E-40 |

To get the probability of getting at least 1 hit in a time of 192 ns, we have to add up the probabilities of getting 1 hit, 2 hits, ….

This results in 3,68 x 10-6

On CH 1 the probability of getting at least 1 hit in a time of 192 ns = 3,68 x10-6

For channel 2 we got the following results:

| CH2: 4074 | hits / min |  |  |
| --- | --- | --- | --- |

The average number of hits in 192 ns is 0.0000130.

The Poisson-distribution:

Δt = 192 ns

| k | Probability | Prob (%) |
| --- | --- | --- |
| 0 | 0.999987 | 99.9987 |
| 1 | 1.30E-05 | 0.00130 |
| 2 | 8.50E-11 | 8.50E-09 |
| 3 | 3.69E-16 | 3.69E-14 |
| 4 | 1.20E-21 | 1.206E-19 |
| 5 | 3.14E-27 | 3.14E-25 |
| 6 | 6.82E-33 | 6.82E-31 |
| 7 | 1.27E-38 | 1.27E-36 |

On CH 2 the probability of getting 1 hit in a time of 192 ns = 1,30 x10-5

Now what is the probability of a coincidence of 2 hits in a time-window of 192 ns?

When there is a coincidence, we have one hit on CH1 AND one hit on CH2.

The probability of getting a coincidence is the product of the probability of having (at least) 1 hit on CH1 and the probability of having 1 hit on CH2:

3,68 x 10-6 x 1,30 x 10-5 = 4,78 x 10-11

A probability of 4,78 x 10-11 in 192 ns, means that we can expect a coincidence in 4017 s = 1h 07 min!

But as we saw, we measured 90 coincidences per 1 min, meaning 1 coincidence in 0,67 s!

predicted: measured 1 coincidence in 1 h 07 min > < 1 coincidence in 0,67 s

When the probability is much higher than predicted, the events are not independent.

Both events (hits) are coupled on a certain way.

In this case the extremely higher frequency can be understood if we assume that many of the particles that hit plate 1 will also pass through plate 2 within a time of 192 ns.

So on statistical ground, we can make acceptable the existence of high energetic particles (i.e. muons) going trough plate 1 and plate 2 on almost the same moment.

- Conclusion

We proved that the number of coincidences is extremely much greater than predicted by statistical analysis, what can make acceptable the existence of high energetic particles (i.e. muons).

- Further investigations

  - Improve the technical equipment to make it possible to measure consecutive times of 192 ns to check the Poissondistribution of the number of hits

  - Investigation what is the cause of non-coincidental hits (spontaneous illumination, other low energetic particles, …)

  - …