# Principle

- The source of the electron beam is the electron gun, which produces a stream of electrons through thermionic emission at the heated cathode and focuses it into a thin beam by the control grid (or “Wehnelt cylinder”).

- A strong electric field between cathode and anode accelerates the electrons, before they leave the electron gun through a small hole in the anode.

- The electron beam can be deflected by a capacitor or coils in a way which causes it to display an image on the screen. The image may represent electrical waveforms (oscilloscope), pictures (television, computer monitor), echoes of aircraft detected by radar etc.

- When electrons strike the fluorescent screen, light is emitted.

- The whole configuration is placed in a vacuum tube to avoid collisions between electrons and gas molecules of the air, which would attenuate the beam.

# Safety precautions

- Don’t touch cathode ray tube and cables during operation, voltages of 300 V are used in this experiment!

- Do not exert mechanical force on the tube, danger of implosions!

# Setup

| Equipment | Assembling the experiment |
| --- | --- |
| Braun’s tube Power supply for Braun tube Power supply, 0...600 V DC Coil, 1200 turns (2x) Coil holder (2x) Support base Support rod , square, L = 400 mm (3x) Right angle clamp (3x) Connecting wires | Connect the sockets of the cathode ray tube to the power supply as shown in the circuit diagram below. To achieve a magnetic deflection of the electron beam setting two series connected coils, 1200 winding, on a coil holder which (possibly with the aid of clamping columns) can be secured to retort stands; the common coil axis should intersect the cathode ray tube between anode and deflector plates. |

# Experimental procedure

- Set the voltage of the auxiliary anode  to 10 V  using the first knob on the DC power supply

- Set the voltage of  the anode to about  30/50 V using the second knob on the DC power supply

- Use the third knob to intensify the beam (200…300 V)

- Modulate the voltage of the anode and the auxiliary anode to get a sharp beam (knob 1+2)

- Switch on the Braun’s tube operation unit

- Build up a time base by increasing frequency and amplitude

# Text boxes

Fluorescent screen

UA

Cathode

Anode

Control grid

!