“Dotted Light” from a single wire

subject:   standing waves  / electromagnetic forces

equipment needed:

- Power supply  (  DC / AC   0 – 20 V  )

- Thin wire  ( any metallic material,

e.g.  Cu   ,  (  = 0,2 mm , 30 cm ( l (  80 cm )

- 2 insulated holding devices

- 2 cables

- U – Magnet

What to do

        - First find out the voltage ( DC ) with which the

wire starts to glow

        - If it doesn’t glow, shorten it’s length to reduce

the resistance

        - Bring the magnet to the wire

        - Change to AC

        - With current flowing the wire will begin to

oscillate ( Lorentz force)

        - Adjust mechanical tension of the wire  (which

will lengthen with increasing temperature ) to

get a certain mode of a standing wave

        - nodes of the wave will glow – antinodes stay

dark because of air cooling by movement of

the wire

Peter Freilinger / HST 2001/ Small Experiment Working Group