Experiment: Converting AC to DC (Rectifiers)

Objectives:

- To investigate the function of a diode

- To convert AC into DC

- To compare different types of rectifiers

- To reduce DC-ripple

Material needed:

1 AC-Power supply (5V- 25V, depending on type of diode)

5 diodes (e.g. 1N4001, 1N4004)

1 electrolyte capacitor C1 (small capacity e.g. 22uF/40V)

1 electrolyte capacitor C2 (big capacity e.g. 1000uF/40V)

2 light bulbs (voltage depending on power supply voltage used)

1 bread board

1 oscilloscope (2 channels)

cables

# Experiment 1: Half-Wave-Rectifier

- Set up circuit 1

- Use oscilloscope to display UAC (channel 1) and UL (channel2)

- Bypass diode with cable 1

- Adjust AC-Power Supply to the chosen voltage

- Switch on AC-Power Supply

- Graph UL for the protocol (UL=UL11)

- Remove cable 1

- Graph UL for the protocol (UL=UL12)

- Add the smaller capacitor C1 to the circuit (parallel to the lamp)

- Graph UL for the protocol (UL=UL1C1)

- Remove capacitor

- Add the larger capacitor C2 to the circuit (parallel to the lamp)

- Graph UL for the protocol (UL=UL1C2)

- Switch off power supply

- Disconnect oscilloscope

- Analyze the resulted graphs

# Experiment 2: Bridge-Rectifier (Full-Wave-Rectifier)

- Set up circuit 2

- Use oscilloscope to display UL

ATTENTION !!! DO NOT MEASSURE UAC AND UL WITH THE OSCILLOSCOPE SIMUNTANOUISLY !!!

Different ground potentials are connected. This can cause damage to the oscilloscope or the electronic circuits.

- Adjust AC-Power Supply to the chosen voltage

- Switch on AC-Power Supply

- Graph UL for the protocol (UL=UL21)

- Add the smaller capacitor C1 to the circuit (parallel to the lamp)

- Graph UL for the protocol (UL=UL2C1)

- Remove capacitor

- Add the larger capacitor C2 to the circuit (parallel to the lamp)

- Graph UL for the protocol (UL=UL2C2)

- Switch off AC-Power Supply

- Analyze the resulted graphs

Explanation:

Setup of the circuits for both types of rectifiers: =>

The following diagrams show photos taken from the screen of a digital oscilloscope. Ground level is indicated by the marks “1” and “2”.

Experiment 1: Half-Wave-Rectifier:

UL11: UL11 = UAC, AC-50Hz Sine Wave, diode bypassed

Voltage without capacitor (UL12):

UAC

UL12

Current in positive direction (anode => cathode, positive half-wave) can pass the diode.

Current in negative direction (negative half-wave) is not able to pass. => only the positive half-wave appears.

Voltage with small capacitor C1 (UL1C1 ):

UAC

UL1C1

Capacitor C1 is charged by the increasing voltage of the positive half-wave and discharged during the decrease of the half-wave and the zero-voltage period. Due to the small capacitance voltage UL1C1 has high ripple.

Voltage with large capacitor C2 (UL1C2):

UAC

UL1C2

Due to the larger capacitance C2 the voltage UL1C2 is not dropping so low

=> ripple is low.

Experiment 2: Bridge-Rectifier (Full-Wave-Rectifier):

ATTENTION !!! DO NOT MEASSURE UAC AND UL WITH THE OSCILLOSCOPE SIMUNTANOUISLY !!!  Here UAC is taken from a saved reference channel !!

Voltage without capacitor (UL21):

UAC

UL21

Positive and negative current can find paths over the diode network. Therefore the negative half-wave is clapped to positive voltage.

Voltage with small capacitor C1 (UL2C1 ):

UAC

UL2C1

Capacitor C1 is charged by the increasing voltage and discharged during the decreasing voltage. Because of the smaller decreasing period the voltage UL2C1 does not drop so much.

Voltage with large capacitor C2 (UL2C2):

UAC

UL2C2

Due to the larger capacitance C2 the voltage is not dropping so low

=> ripple is low.

Conclusion:

The two methods converting AC to DC are shown =>

Top to bottom:

- Supplied AC-Voltage

- Half-Wave-Rectifier

- Bridge-rectifier

The ripple can be decreased by using capacitors.

This experiment was designed and presented at

CERN, HST-2002 programme by:

Dipl.-Ing. Dr. Gerd Vogt

Hoehere Lehranstalt fuer Umwelt und Wirtschaft

3683 Yspertal, Austria

http://www.hlaysper.ac.at

gvogt@hlaysper.ac.at

# Text boxes

Cable 1

UL

UAC

AC

UL

UAC

AC

Full-Wave

Half-Wave