Experiment: Speed of Muons (PART 2)

- Aim of the experiment:

The aim of the experiment is to determine the speed of muons reaching the Earths’ surface. We will use the Cosmic Ray equipment available from Quarknet (Thomas Jordan).

- Equipment and setup:

We used

  - two scintillator plates, each having a photomultipliertube (PMT)

  - Data Acquisition Card (DAC) developed by Quarknet

  - GPS receiver

  - pc

DAC

Totally four scintillatorplates can be connected with the DAC, of which we will use two.

- Procedure

We placed the plates one above the other at a distance of 0,645 m (± 0,005 m)

The Data Acquisition was triggered as follows:

when the first plate was hit, a time-window of 192 ns ( = 8 x 24 ns) was opened.

If a second hit was registered in this time, both hits were registered (= coincidence).

If no second hit was registered in this time, the first hit was ejected.

Beside other data, the channel number and the time of the rising edge for both hits (t1 and t2) were registered.

Finally, we got series of (hexadecimal) data:

| (1) | (2) | (3) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) | (12) | (13) | (14) | (15) | (16) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 309AEF47 | 80 | 1 | 0 | 1 | 2F | 1 | 2E | 1 | 2EFD7017 | 123044.531 | 130706 | A | 6 | 0 | 395 |
| 30C82C76 | 80 | 1 | 0 | 1 | 3A | 1 | 32 | 1 | 2EFD7017 | 123044.531 | 130706 | A | 6 | 0 | 395 |
| 30DCEB70 | 80 | 1 | 0 | 1 | 0 | 1 | 3F | 1 | 2EFD7017 | 123045.531 | 130706 | A | 6 | 0 | -604 |
| 30DCEB71 | 0 | 1 | 0 | 1 | 29 | 3D | 1 | 0 | 2EFD7017 | 123045.531 | 130706 | A | 6 | 0 | -604 |
| 312D8B10 | 80 | 1 | 0 | 1 | 3D | 1 | 3B | 1 | 2EFD7017 | 123045.531 | 130706 | A | 6 | 0 | -604 |
| 31928591 | 80 | 1 | 0 | 1 | 0 | 1 | 3E | 1 | 31793859 | 123045.531 | 130706 | A | 6 | 0 | 396 |
| 31928592 | 0 | 1 | 0 | 1 | 2F | 1 | 1 | 0 | 31793859 | 123045.531 | 130706 | A | 6 | 0 | 396 |
| 31C75784 | 80 | 1 | 0 | 1 | 3E | 1 | 3F | 1 | 31793859 | 123045.531 | 130706 | A | 6 | 0 | 396 |
| 321C4A31 | 80 | 1 | 0 | 1 | 3F | 1 | 0 | 1 | 31793859 | 123045.531 | 130706 | A | 6 | 0 | 396 |
| 321C4A32 | 0 | 1 | 0 | 1 | 1 | 0 | 24 | 1 | 31793859 | 123045.531 | 130706 | A | 6 | 0 | 396 |
| 3278ECEB | 80 | 1 | 0 | 1 | 0 | 1 | 36 | 1 | 31793859 | 123045.531 | 130706 | A | 6 | 0 | 396 |
| 3278ECEC | 0 | 1 | 0 | 1 | 21 | 1 | 1 | 0 | 31793859 | 123045.531 | 130706 | A | 6 | 0 | 396 |
| … |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

- =

- =

- =

- =

- =

- =

- =

- =

- =

- =

- =

- =

- =

- =

- =

- =

The hexadecimal data were converted into decimal numbers.

The time differences between (consecutive) rising edges on CH1 and on CH2 were calculated.

We imported these time-differences in EXCEL, made a histogram of them, calculated the average and the standarddeviation.

- Results

In totally 1428 data were held back.

| number of time differences = | 1428 |
| --- | --- |
| MIN = | 0.491 ns |
| MAX = | 11.748 ns |
| AVERAGE = | 3.422 ns |
| STDEV = | 2.187 ns |

Calculation of the speed of the muons results in

v = Δx / Δt = 0,645 m / 3,422 ns = 1,88 x 108 m/s

Calculation of the error on the speed results in

verr = 1,20 x 108 m/s

v = (1,88 ± 1,20) x 108 m/s

The error on the speed is great (64 %!).

- Analyze of the result

We expected a graph combined of two effects:

  - the time between 2 coincidences NOT caused by muons, but other way (individual hits on plate 1 and plate 2, decay between the plates, spontaneous illumination ...  ) is supposed to be homogeneous distributed

  - the time between 2 coincidences caused by muons will give a narrow peak (when all the muons travel with almost the same speed)

  - the series of data of both kind will give a graph as below

The distribution we got is shown in next graph.

Most of the time-diffs are between 0 and 6 ns, but the peak is less more sharp than expected.

Possible expanations of this phenomena are:

  - not all the muons travel with the same speed

  - the error on the time-differences is great

The last explanation applies, because the time-differences between the rising edges of the hits are small (in the order of a few nanoseconds) and the error on those time-differences are in the order of 1 ns.

This may well be seen in the result of the following experiment, in which the two plates were in together. In the case of an infinily accurate measurement the time-difference should be zero. As it is not, the distribution will give the error on the time-differences.

ref: IEEE Trans.Nucl.Sci. 51 (2004) 926-930

Finally, we got an average time-difference of  3.422 ns ± 2.187 ns. This is 64 %.

The error on the speed is the same.

This may not surprise, because the error on the distance is neglectible compared with the error on the time-differences.

If we could measure the time-differences as accurate as the distance, we should have an error on the speed as low as 0,020 x 108 m/s!

- Conclusion

The speed of the muons reaching the earths’ surface is

v = (1,88 ± 1,20) x 108 m/s

The great error on the speed is caused by the error of 1 ns on the measurement of the time-differences.

- Further investigations and improvement of the experiment

  - Investigation of the question ‘have all the muons reaching the earths’ surface the same speed, and within which limits?’

  - The experiment could be improved in different ways or other experiments could be done:

    - Improve the technical equipment to reduce the error on the time-differences

    - Improve the experiment by putting the plates on a greater distance of each other: the time-diffs will be greater, resulting in a smaller relative error

    - Another experiment:
use a distance of e. g. 2,00 m, a time-window of e.g. 192 ns and measure the average number of coincidences per minut for that time-window.
Reduce the time-window and repeat the experiment. When the time-window is smaller than the time the muons need to travel the distance, the average number of coincidences per minut will dramatically drop down. The time-window where this happens gives the traveltime of the muons.

    - Another experiment:
see: http://scienzapertutti.lnf.infn.it/FotoCrescere/relazioni/LNF_mihai_viteazul.ppt